## Slide 1: Computer Networks
CSE3101 · Lecture 1 — Introduction & Motivation

## Slide 2
Course Contents
Introduction, history, and development of computer networks
Layered architecture — the OSI Model and TCP/IP Model
Application Layer: basic communication applications and protocols
Transport Layer: services, protocols, and reliable protocol design
Network Layer: services, routing algorithms, addressing, sub-networks
Link Layer: channel access, addressing, interconnection devices
Physical Layer: physical media, data communication basics, line encoding
Wireless LAN, IEEE 802.11, 3G/4G, and Wireless Sensor Networks
Reference: Kurose & Ross — Computer Networking: A Top-Down Approach (6e)
Reference: Tanenbaum — Computer Networks (4e) · Forouzan & Mosharraf — Computer Networks: A Top-Down Approach

## Slide 3
What Is a Computer Network?
A network is a set of devices (often called nodes) connected by communication links.
A node can be a computer, printer, or any other device capable of sending and/or receiving data.
A link can be a cable, air, optical fiber, or any medium that can carry a signal carrying information.

## Slide 4
Layers of Identification on a Network
Network — identified using the Network ID (NetId)
Host — identified using the Host ID (HostId)
Process — identified using the Port Number
  Together, NetId + HostId form the device's IP address (e.g. 192.68.42.42)
Application-layer protocols such as DNS, HTTP, and SMTP operate on top of this addressing
  DNS converts a human-readable name into an IP address — this adds a small overhead

## Slide 5
Network Criteria
Performance:
  Depends on the network elements involved
  Measured in terms of delay and throughput
Reliability:
  Failure rate of network components
  Measured in terms of availability and robustness
Security:
  Protecting data from corruption or loss due to errors or malicious users

## Slide 6
Type of Connection
Point-to-Point:
  A single transmitter and a single receiver
Multipoint:
  Multiple recipients share a single transmission
Physical Topology:
  How devices are physically connected to one another
Type of Transmission:
  Unicast — web browsing, email
  Multicast — online gaming, live webinars
  Broadcast — Wi-Fi setup, telecast

## Slide 7
Protocol
A protocol is synonymous with a rule.
It consists of a set of rules that govern data communication.
It determines what is communicated, how it is communicated, and when it is communicated.
The key elements of a protocol are syntax, semantics, and timing.

## Slide 8
Elements of a Protocol
Syntax
Structure or format of the data. Indicates how to read the bits — field delineation.
Semantics
Interprets the meaning of the bits. Knows which fields define what action.
Timing
When data should be sent, and at what speed — and when it is expected to be received.

## Slide 9
Motivation: The Information Economy
Today's economy is built not just on creating, distributing, and retailing goods —
— but increasingly on creating, distributing, and retailing information itself.
The future economy is likely to be dominated by information.

## Slide 10
What Is Information?
Everyday information takes many forms: books, bills, CDs, and more.
It can exist in analog form (atoms) or digital form (bits).
Converting information from atoms to bits lets us use networks to move it — instead of moving physical atoms.
  This conversion is the foundation of modern data communication.

## Slide 11
The Challenges
Represent all types of information as bits.
Move those bits:
  In large quantities
  Everywhere
  Cheaply
  Securely
  With guaranteed quality of service

## Slide 12
Today's Networks Are Complex
Modern networks already involve many interconnected systems, protocols, and devices.
Tomorrow's networks will be even more complex.
This course's challenge: build a solid foundation for understanding how it all fits together — layer by layer.