## Slide 1: Data Link layer

## Slide 2: Data Link Layer
Understanding the Bridge Between Physical and Network Layers
"Acts as the neighbourhood traffic cop of network communication“
Position: Between Physical Layer (Layer 1) and Network Layer (Layer 3) Primary Purpose: Ensure reliable data transfer between directly connected nodes Scope: Local delivery within the same network segment Key Responsibility: Node-to-node delivery with error detection and flow control

## Slide 3: Data Link Layer
Core Responsibilities of Data Link Layer
Framing - Organizing bits into manageable frames
Addressing - Physical addressing using MAC addresses
Error Detection & Correction - Ensuring data integrity
Flow Control - Managing data transmission rate
Access Control - Managing shared medium access
Synchronization - Coordinating sender and receiver

## Slide 4: Data Link Layer
Data Link Layer Sub-layers
Logical Link Control (LLC)
• Upper sub-layer • Protocol multiplexing and demultiplexing • Flow control and error checking • Interface between MAC and Network Layer
Media Access Control (MAC)
• Lower sub-layer • Physical addressing (MAC addresses) • Media access management • Frame encapsulation and validation
Notes: Multiplexing is the process of combining multiple data streams or applications into a single stream for transmission over the network.
Demultiplexing is the process of separating the received combined stream back into individual application data streams.

## Slide 5: Data Link Layer
LLC Sub-layer Functions
• Multiplexing: Multiple protocols over MAC layer
• Flow Control: Coordinates data transmission rate
• Error Control: Detects frame loss and requests retransmission
Acknowledgment Tracking: Monitors successful frame delivery
Interface Role: Acts as bridge between upper layers and MAC sub-layer

## Slide 6: Data Link Layer
MAC Sub-layer Functions
Media Access Control Details
Core Functions:
• Physical Addressing: Unique MAC address identification
• Frame Encapsulation: Adds headers and trailers
• Medium Access: Coordinates shared channel usage
• Collision Management: Handles multiple access scenarios
MAC Address: 48-bit unique identifier assigned at manufacturing

## Slide 7: Data Link Layer
Framing Process
Converting Packets to Frames
What is Framing? • Dividing data into manageable units called frames • Adding headers and trailers for identification and control • Enabling frame boundary recognition
Frame Structure: • Header: Source/destination addresses, control information • Payload: Actual data from upper layers • Trailer: Error detection bits, end markers

## Slide 8: Data Link Layer
Types of Framing
Fixed vs Variable Size Framing
Fixed-Size Framing
• Characteristics: Constant frame size • Advantages: Simple boundary detection • Examples: ATM cells (53 bytes) • Use Cases: Wide Area Networks (WAN)
Variable-Size Framing
• Characteristics: Flexible frame sizes • Boundary Methods: Length fields or delimiters • Examples: Ethernet frames • Use Cases: Local Area Networks (LAN)

## Slide 9: Data Link Layer
Error Types
Single-Bit Errors
• Only one bit changed during transmission • Example: 1010 becomes 1000 • Common in high-quality channels
Burst Errors
• Multiple consecutive bits corrupted • Example: 1011101 becomes 1000001 • Common in wireless environments • More challenging to detect and correct

## Slide 10: Data Link Layer
Error Detection Techniques: Ensuring Data Integrity
Hamming Distance
Count the number of dissimilar bits of the given 2 numbers
Simple/Single Parity Check
Adds a single parity bit
Detects single-bit errors only
Even or odd parity systems
Checksum
Mathematical sum of data segments
Detects multiple-bit errors
1's complement arithmetic

## Slide 11: Data Link Layer
Cyclic Redundancy Check (CRC)
• Polynomial-based error detection • Highly effective for burst errors • Widely used in modern networks

## Slide 12: SIMPLE/ SINGLE PARITY CHECK
Parity means in terms of the count of 1’s
Two types: Odd and Even
In this technique, a redundant bit called a parity bit is appended to every data unit so that the number of 1’s in the unit, including the parity, becomes even.
Blocks of data from the source are subjected to a check bit or parity bit generator form, where a parity of:
    1 is added to the block if it contains an odd number of 1’s, and
    0 is added if it contains an even number of 1’s.
This scheme makes the total number of 1’s even, which is why it is called even parity checking.

## Slide 14: Checksum (CHECK THE SUM)
Sender’s End:
The data is divided into k segments, each of m bits.
On the sender’s end, the segments are added using 1’s complement arithmetic to get the sum.
The sum is complemented to get the checksum.
The checksum segment is sent along with the data segments.
Receiver’s End:
At the receiver’s end, all received segments are added using 1’s complement arithmetic to get the sum. The sum is complemented.
If the result is zero, the received data is accepted; otherwise, it is discarded.

## Slide 15
Performance
The checksum detects all errors involving an odd number of bits.
It also detects most errors involving an even number of bits.

## Slide 17: Cyclic Redundancy Check (CRC)
CRC is the most powerful and easiest to implement technique
CRC is based on binary division.
The divisor is generated using polynomials.
It is commonly used to detect accidental changes to data transmitted via telecommunications networks and storage devices.

## Slide 18
The sender performs a division operation on the bits being sent and calculates the remainder.
Before sending the actual bits, the sender adds the remainder at the end of the actual bits.
Actual data bits plus the remainder are called a codeword. The sender transmits data bits as codewords.
At the other end, the receiver performs a division operation on codewords using the same CRC divisor.
If the remainder contains all zeros, the data bits are accepted; otherwise, it is considered that some data corruption occurred in transit.

## Slide 20: Data Link Layer
Access Control Methods: Managing Shared Medium Access
CSMA/CD (Collision Detection)
• Used in wired Ethernet networks • Listen before transmitting • Detect collisions and retransmit • Process: Sense → Transmit → Detect → Backoff → Retry
CSMA/CA (Collision Avoidance)
• Used in wireless networks (WiFi) • Avoid collisions through coordination • Mechanisms: RTS/CTS, Interframe spacing

## Slide 21: Data Link Layer
CSMA/CD vs CSMA/CA
Aspect | CSMA/CD | CSMA/CA
Usage | Wired Ethernet | Wireless Networks
Collision Handling | Detect after occurrence | Avoid before occurrence
Efficiency | Higher throughput | Lower overhead in wireless
Complexity | Simpler | More complex protocols
Reliability | Direct collision detection | Acknowledgment-based

## Slide 22: Data Link Layer
When nodes or stations are connected and use a common link, called a multipoint or broadcast link, a multiple-access protocol is needed to coordinate access to the link.
The problem of controlling access to the medium is like the rules of speaking in an assembly.
The procedures guarantee that the right to speak is upheld and ensure that two people do not talk at the same time, do not interrupt each other, do not monopolize the discussion, and so on

## Slide 23
Data link layer divided into two functionality-oriented sublayers
Or Logical link control and MAC

## Slide 24
Taxonomy of multiple-access protocols discussed in this chapter

## Slide 25
RANDOM ACCESS
In random access or contention methods, no station is superior to another station, and none is assigned the control over another. No station permits, or does not permit, another station to send. At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
ALOHA Carrier Sense Multiple Access
Carrier Sense Multiple Access with Collision Detection
Carrier Sense Multiple Access with Collision Avoidance
Topics discussed in this section:

## Slide 26: Random Access
In random-access or contention methods, no station is superior to another station, and none is assigned control over another.
At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
This decision depends on the state of the medium (idle or busy). In other words, each station can transmit when it desires on the condition that it follows the predefined procedure, including testing the state of the medium.

## Slide 27: Random Access
Two features give this method its name.
First, there is no scheduled time for a station to transmit. Transmission is random among the stations.
That is why these methods are called random access.
Second, no rules specify which station should send next. Stations compete with one another to access the medium.
That is why these methods are also called contention methods.

## Slide 28: Random Access
In a random-access method, each station has the right to the medium without being controlled by any other station.
However, if more than one station tries to send, there is an access conflict—collision—and the frames will be either destroyed or modified.
To avoid access conflict or to resolve it when it happens, each station follows a procedure that answers the following questions:
When can the station access the medium?
What can the station do if the medium is busy?
How can the station determine the success or failure of the transmission?
What can the station do if there is an access conflict?

## Slide 29: ALOHA
ALOHA, the earliest random-access method, was developed at the University of Hawaii in early 1970.
It was designed for a radio (wireless) LAN, but it can be used on any shared medium.
It has an acknowledgement used for successful communication.
There are potential collisions in this arrangement. The medium is shared between the stations.
When a station sends data, another station may attempt to do so at the same time. The data from the two stations collide and become garbled.

## Slide 30: Pure ALOHA
The original ALOHA protocol is called pure ALOHA.
This is a simple but elegant protocol. The idea is that each station sends a frame whenever it has a frame to send (multiple access).
However, since there is only one channel to share, there is the possibility of collision between frames from different stations.
Consider only Transmission time (No propagation time).

## Slide 31
Frames in a pure ALOHA network

## Slide 32: Pure ALOHA
The pure ALOHA protocol relies on acknowledgments from the receiver. When a station sends a frame, it expects the receiver to send an acknowledgment.
If the acknowledgment does not arrive after a time-out period, the station assumes that the frame (or the acknowledgment) has been destroyed and resends the frame.
A collision involves two or more stations. If all these stations try to resend their frames after the time-out, the frames will collide again.
Transmission Time = Message length/ Bandwidth

## Slide 33: Pure ALOHA
Pure ALOHA dictates that when the time-out period passes, each station waits a random amount of time before resending its frame. The randomness will help avoid more collisions.
We call this time the backoff time, TB.
The backoff time TB is a random value that normally depends on K (the number of attempted unsuccessful transmissions).
Propagation time is the time required for a frame to travel from source to destination, Tp
The time-out period is equal to the maximum possible round-trip propagation delay, which is twice the amount of time required to send a frame between the two most widely separated stations
Time Period = 2 × Tp.

## Slide 34
Procedure for pure ALOHA protocol

## Slide 35
The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find
Tp = (600 × 105 ) / (3 × 108 ) = 2 ms.
Now we can find the value of TB for different values of K .
a. For K = 1, the range is {0, 1}. The station needs to
generate a random number with a value of 0 or 1. This means that TB is either 0 ms (0 × 2) or 2 ms (1 × 2), based on the outcome of the random variable.
Example 12.1

## Slide 36
b. For K = 2, the range is {0, 1, 2, 3}. This means that TB can be 0, 2, 4, or 6 ms, based on the outcome of the random variable.
c. For K = 3, the range is {0, 1, 2, 3, 4, 5, 6, 7}. This means that TB can be 0, 2, 4, . . . , 14 ms, based on the outcome of the random variable.
d. We need to mention that if K > 10, it is normally set to 10.
Example 12.1 (continued)

## Slide 37
Vulnerable time for pure ALOHA protocol
the length of time in which there is a possibility of collision.
The stations send fixed-length frames with each frame taking Tfr seconds to send.

## Slide 38: ALOHA
Vulnerable time during which a collision may occur in pure ALOHA is 2 times the frame transmission time.
Pure ALOHA vulnerable time = 2 × Tfr or ( 2 × Tt )
Throughput Let us call G the average number of frames generated by the system during one frame transmission time.
Then it can be proven that the average number of successfully transmitted frames for pure ALOHA is S = G × e −2G

## Slide 39
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Example 12.2
Solution
Average frame transmission time Tfr is 200 bits/200 kbps or 1 ms. The vulnerable time is 2 × 1 ms = 2 ms.
This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the one 1-ms period that this station is sending.

## Slide 40
The throughput for pure ALOHA is S = G × e −2G .
The maximum throughput
Smax = 0.184 when G= (1/2).
Note

## Slide 41: Calculation of max efficiency/ throughput Pure ALOHA
S = G × e −2G
Differentiate it with respect to G
G × e−2G (-2) + e−2G (1) = 0 ; (to find the maximum value)
= e−2G (-2G+1) =0
=(-2G+1) =0
= G =1/2
Now, solve the efficiency equation
Max efficiency (Smax) = 0.184

## Slide 42
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Example 12.3
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−2 G or S = 0.135 (13.5 percent). This means that the throughput is 1000 × 0.135 = 135 frames. Only 135 frames out of 1000 will probably survive.

## Slide 43
Example 12.3 (continued)
b. If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e −2G or S = 0.184 (18.4 percent). This means that the throughput is 500 × 0.184 = 92 and that only 92 frames out of 500 will probably survive. Note that this is the maximum throughput case, percentagewise.
c. If the system creates 250 frames per second, this is (1/4) frame per millisecond. The load is (1/4). In this case S = G × e −2G or S = 0.152 (15.2 percent). This means that the throughput is 250 × 0.152 = 38. Only 38 frames out of 250 will probably survive.

## Slide 44: Slotted ALOHA
Pure ALOHA has a vulnerable time of 2 × Tfr.
This is so because there is no rule that defines when the station can send.
A station may send soon after another station has started or just before another station has finished.
Slotted ALOHA was invented to improve the efficiency of pure ALOHA.
In slotted ALOHA we divide the time into slots of Tfr seconds and force the station to send only at the beginning of the time slot.

## Slide 45
Because a station is allowed to send only at the beginning of the synchronized time slot, if a station misses this moment, it must wait until the beginning of the next time slot.
This means that the station which started at the beginning of this slot has already finished sending its frame.
Of course, there is still the possibility of collision if two stations try to send at the beginning of the same time slot.
However, the vulnerable time is now reduced to one-half, equal to Tfr.

## Slide 46
Figure 12.6 Frames in a slotted ALOHA network

## Slide 47
Figure 12.7 Vulnerable time for slotted ALOHA protocol

## Slide 48
Slotted ALOHA vulnerable time = Tfr or (2 × Tt )
Throughput It can be proven that the average number of successful transmissions for slotted ALOHA is:
S= G × e−G.
The maximum throughput Smax is 0.368, when G = 1.

## Slide 49
The throughput for slotted ALOHA is S = G × e−G .
The maximum throughput Smax = 0.368 when G = 1.
Note

## Slide 50
A slotted ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput of the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Example 12.4
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−G or S = 0.368 (36.8 percent). This means that the throughput is 1000 × 0.0368 = 368 frames. Only 386 frames out of 1000 will probably survive.

## Slide 51
Example 12.4 (continued)
b. If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e−G or S = 0.303 (30.3 percent). This means that the throughput is 500 × 0.0303 = 151. Only 151 frames out of 500 will probably survive.
c. If the system creates 250 frames per second, this is (1/4) frame per millisecond. The load is (1/4). In this case S = G × e −G or S = 0.195 (19.5 percent). This means that the throughput is 250 × 0.195 = 49. Only 49 frames out of 250 will probably survive.

## Slide 52: CSMA
In other words, CSMA is based on the principle “sense before transmit” or “listen before talk.”
To minimize the chance of collision and, therefore, increase the performance, the CSMA method was developed.
The chance of collision can be reduced if a station senses the medium before trying to use it.
Carrier sense multiple access (CSMA) requires that each station first listen to the medium (or check the state of the medium) before sending.
CSMA can reduce the possibility of collision, but it cannot eliminate it.

## Slide 53
The possibility of collision still exists because of propagation delay; when a station sends a frame, it still takes time (although very short) for the first bit to reach every station and for every station to sense it.
In other words, a station may sense the medium and find it idle, only because the first bit sent by another station has not yet been received.

## Slide 54
Figure 12.8 Space/time model of the collision in CSMA

## Slide 55
Figure 12.9 Vulnerable time in CSMA

## Slide 56
Figure 12.10 Behavior of three persistence methods

## Slide 57: Kinds of CSMA
CSMA
Nonpersistent CSMA
Persistent CSMA
Unslotted Nonpersistent CSMA
Unslotted persistent CSMA
Slotted Nonpersistent CSMA
Slotted persistent CSMA
1-persistent CSMA
p-persistent CSMA

## Slide 58: Nonpersistent/x-persistent CSMA Protocols
Nonpersistent (0 persistant) CSMA Protocol:
Step 1: If the medium is idle, transmit immediately
Step 2: If the medium is busy, wait a random amount of time and repeat Step 1
  Random backoff reduces probability of collisions
  Waste idle time if the backoff time is too long
1-persistent CSMA Protocol:
Step 1: If the medium is idle, transmit immediately
Step 2: If the medium is busy, continue to listen until medium becomes idle, and then transmit immediately
  There will always be a collision if two nodes want to retransmit
  (usually you stop transmission attempts after few tries)

## Slide 59
Figure 12.11 Flow diagram for three persistence methods

## Slide 60: Nonpersistent/x-persistent CSMA Protocols
p-persistent CSMA Protocol:
Step 1: If the medium is idle, transmit with probability p, and delay for worst case propagation delay for one packet with probability (1-p)
Step 2: If the medium is busy, continue to listen until medium becomes idle, then go to Step 1
Step 3: If transmission is delayed by one time slot, continue with Step 1
  A good tradeoff between nonpersistent and 1-persistent CSMA

## Slide 61: How to Select Probability p ?
Assume that N nodes have a packet to send and the medium is busy
Then, Np is the expected number of nodes that will attempt to transmit once the medium becomes idle
If Np > 1, then a collision is expected to occur
Therefore, network must make sure that Np < 1 to avoid collision, where N is the maximum number of nodes that can be active at a time

## Slide 62: Throughput
0 1 2 3 4 5 6 7 8 9
G
1.0
0.9
0.8
0.7
0.6
0.5
0.4
0.3
0.2
0.1
0
S
Aloha
Slotted Aloha
1-persistent CSMA
0.5-persistent CSMA
0.1-persistent CSMA
0.01-persistent CSMA
Nonpersistent CSMA

## Slide 63
Figure 12.12 Collision of the first bit in CSMA/CD

## Slide 64
Figure 12.13 Collision and abortion in CSMA/CD

## Slide 65
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal, as we see later) is 25.6 μs, what is the minimum size of the frame?
Example 12.5
Solution
The frame transmission time is Tfr = 2 × Tp = 51.2 μs. This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision. The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet.

## Slide 66
Figure 12.14 Flow diagram for the CSMA/CD

## Slide 67
Figure 12.15 Energy level during transmission, idleness, or collision

## Slide 68
Figure 12.16 Timing in CSMA/CA

## Slide 69
In CSMA/CA, the IFS can also be used to define the priority of a station or a frame.
Note

## Slide 70
In CSMA/CA, if the station finds the channel busy, it does not restart the timer of the contention window;
it stops the timer and restarts it when the channel becomes idle.
Note

## Slide 71
Figure 12.17 Flow diagram for CSMA/CA

## Slide 72
12-2 CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations. We discuss three popular controlled-access methods.
Reservation Polling Token Passing
Topics discussed in this section:

## Slide 73
Figure 12.18 Reservation access method

## Slide 74
Figure 12.19 Select and poll functions in polling access method

## Slide 75
Figure 12.20 Logical ring and physical topology in token-passing access method

## Slide 76
12-3 CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations. In this section, we discuss three channelization protocols.
Frequency-Division Multiple Access (FDMA) Time-Division Multiple Access (TDMA)
Code-Division Multiple Access (CDMA)
Topics discussed in this section:

## Slide 77
Figure 12.21 Frequency-division multiple access (FDMA)

## Slide 78
In FDMA, the available bandwidth of the common channel is divided into bands that are separated by guard bands.
Note

## Slide 79
Figure 12.22 Time-division multiple access (TDMA)

## Slide 80
In TDMA, the bandwidth is just one channel that is timeshared between different stations.
Note

## Slide 81
In CDMA, one channel carries all transmissions simultaneously.
Note

## Slide 82
Figure 12.23 Simple idea of communication with code

## Slide 83
Figure 12.24 Chip sequences

## Slide 84
Figure 12.25 Data representation in CDMA

## Slide 85
Figure 12.26 Sharing channel in CDMA

## Slide 86
Figure 12.27 Digital signal created by four stations in CDMA

## Slide 87
Figure 12.28 Decoding of the composite signal for one in CDMA

## Slide 88
Figure 12.29 General rule and examples of creating Walsh tables

## Slide 89
The number of sequences in a Walsh table needs to be N = 2m.
Note

## Slide 90
Find the chips for a network with
a. Two stations b. Four stations
Example 12.6
Solution
We can use the rows of W2 and W4 in Figure 12.29:
a. For a two-station network, we have [+1 +1] and [+1 −1].
b. For a four-station network we have [+1 +1 +1 +1], [+1 −1 +1 −1], [+1 +1 −1 −1], and [+1 −1 −1 +1].

## Slide 91
What is the number of sequences if we have 90 stations in our network?
Example 12.7
Solution
The number of sequences needs to be 2m. We need to choose m = 7 and N = 27 or 128. We can then use 90 of the sequences as the chips.

## Slide 92
Prove that a receiving station can get the data sent by a specific sender if it multiplies the entire data on the channel by the sender’s chip code and then divides it by the number of stations.
Example 12.8
Solution
Let us prove this for the first station, using our previous four-station example. We can say that the data on the channel D = (d1 ⋅ c1 + d2 ⋅ c2 + d3 ⋅ c3 + d4 ⋅ c4). The receiver which wants to get the data sent by station 1 multiplies these data by c1.

## Slide 93
Example 12.8 (continued)
When we divide the result by N, we get d1 .