## Slide 1: We will assume that …
Activity is overlapped in time where possible
  PC increment and instruction fetch from memory?
  Instruction decode and effective address calculation
Load-store ISA: the only instructions that take operands from memory are loads & stores
Main memory delays are not typically seen by the processor
  Otherwise the timeline is dominated by them
  There is some hardware mechanism through which most memory access requests can be satisfied at processor speeds (cache memory)

## Slide 2: Term: Processor Cycle Time
Unit of timescale of processor; time required to do a basic operation

## Slide 3: Steps in Instruction Execution
Fetch instruction from memory to processor
IR = Memory[PC]
Increment PC
Decode instruction and get its operands
Decode
Write result to destination register
cache memory access
(simple) ALU operation
(simple) logic circuitry
register access
Get Operands from registers
Execute the operation
  Trigger appropriate functional hardware ALU operation
Load/store: get data from main memory
Write back the result
cache access
register access

## Slide 4: Term: Processor Cycle Time
Unit of timescale of processor; time required to do a basic operation
  Cache memory access
  Register access + some logic (like decode)
  ALU operation

## Slide 5: Steps in Instruction Execution
Fetch instruction from memory to processor
IR = Memory[PC]; Increment PC
Decode instruction and get its operands
Decode; Get Operands from registers
Execute the operation
Trigger appropriate functional hardware
Load/store: get data from main memory
Write back the result
Write result to destination register
1 cycle
1 cycle
1 cycle
1 cycle
1 cycle

## Slide 6: Steps in Execution:JR R6
Fetch instruction from memory to processor
IR = Memory[PC]; Increment PC
Decode instruction and get its operands
Decode; Get Operands from registers
Execute the operation
Trigger appropriate functional hardware
Load/store: get data from main memory
Write back the result
Write result to destination register
1 cycle
1 cycle
1 cycle
1 cycle
1 cycle

## Slide 7: Steps in Execution: ADD R1, R2, R3
Fetch instruction from memory to processor
IR = Memory[PC]; Increment PC
Decode instruction and get its operands
Decode; Get Operands from registers
Execute the operation
Trigger appropriate functional hardware
Load/store: get data from main memory
Write back the result
Write result to destination register
1 cycle
1 cycle
1 cycle
1 cycle
1 cycle

## Slide 8: Steps in Execution: LW R1, -8(R29)
Fetch instruction from memory to processor
IR = Memory[PC]; Increment PC
Decode instruction and get its operands
Decode; Get Operands from registers
Execute the operation
Trigger appropriate functional hardware
Load/store: get data from main memory
Write back the result
Write result to destination register
1 cycle
1 cycle
1 cycle
1 cycle
1 cycle

## Slide 9: Term: Processor Cycle Time
Unit of timescale of processor; time required to do a basic operation
  Cache memory access
  Register access + some logic (like decode)
  ALU operation
A MIPS 1 instruction can be processed in 3-5 cycles
  Jump: IFetch, Decode/OpFetch, WriteReg (3)
  ALU: IFetch, Decode/OpFetch, DoOp, WriteReg (4)
  Load: IFetch, Decode, EffAddr, Cache, WriteReg (5)
Addressing modes: (R) vs d(R)

## Slide 10: Instruction Execution
Mem
IR
+
PC
NPC
4
Instruction Fetch (IF)
from program memory
to instruction register
IR Mem [PC]
Increment PC
Instr Fetch

## Slide 11: Instruction Execution.
Instr Fetch
Reg File
sign extend
A
Imm
B
Instr Decode
Inst Mem
IR
+
PC
NPC
4
A B
Imm
RegisterFile[IRrs] RegisterFile[IRrt]
sign extend(IR15-0)
Instruction Decode & Operand Fetch (ID)

## Slide 12: Instruction Execution..
Execution (EX)
Arithmetic Inst:
ALU-Out ALU-Out
A op B
A op Imm
Load/Store Inst: ALU-Out A + Imm Branch Inst:
ALU-Out NPC + Imm
Jump Inst:
PC NPC 31-28 || IR 25-0 ||00
ALU-
out
ALU
Zero?
Imm
NPC
A
B
Cond.
Execution

## Slide 13: Instruction Execution…
Memory (MEM)
Execution
Memory
ALU
out
ALU
Zero?
Mem
LMD
B
Imm
NPC
A
Cond
Store Instr
Mem[ALUOut] B
Load Instr
LMD
Mem[ALUout]

## Slide 14: Instruction Execution….
Write Back (WB)
ALU Inst
RegisterFile[rd]
Load Inst
RegisterFile[rt]
ALUout
LMD
Conditional Branch Inst PC ALU-out if Cond PC NPC otherwise

## Slide 15: Inside the Processor
Mem
IR
+
PC
NPC
Reg
File
sign extend
A
Imm
B
Inst Fetch IF
Inst Decode ID
4
ALU
out
ALU
Zero?
Mem
LMD
Execution EX
Cond
Memory MEM WB

## Slide 16: Reality Check
Problem: There could be many programs running on a machine concurrently
Sharing the resources of the computer
  Processor time
  Main memory
They must be protected from each other
  One program should not be able to access the variables of another
  This is typically done through Address Translation

## Slide 17: Use of Main Memory by a Program
Instructions (code, text)
Data
  Statically allocated
  Stack allocated
  Heap allocated
text | 
data | 
stack | 
heap | 
0
232 - 1

## Slide 18: Idea of Address Translation
Each program is compiled to use addresses in the range 0 .. MaxAddress (e.g., 0 .. 232 - 1)
These addresses are not real, but only Virtual Addresses
They have to be translated into actual main memory addresses
The translation can be done to ensure that one program can not access variables of another program
Many programs in execution can then safely share main memory
Terminology: virtual address, physical address
Memory Management Unit (MMU): The hardware that does the address translation

## Slide 19: Recal: Basic Computer Organization
Cache
Memory
I/O
Bus
I/O
I/O
MMU
ALU
Register
CPU
Contro
s
l