## Slide 1: High Performance Computing Lecture 6
Matthew Jacob Indian Institute of Science

## Slide 2: MULT Instruction
The product could be twice as large (i.e., 64b)
It may not fit into a single general purpose register
MIPS 1 Solution: Put the 32 least significant bits of the product in LO and the rest in HI
For DIV: quotient in LO, remainder in HI
Example: MULT R1, R2
32 bits
R1 R2
32 bits

## Slide 3: Control Transfer Instructions
 | Mnemonics | Example | Meaning
Conditional Branch | BEQ, BNE, BGEZ, BLEZ, BLTZ, BGTZ | BLTZ R2, -16 | If R2 < 0, PC  PC + 4 -16
Jump | J, JR | J target26 | PC  (PC)31-28¦¦ target26¦¦00
Jump and Link | JAL, JALR | JALR R2 | R31  PC + 8 PC  R2
System call | SYSCALL | SYSCALL | 
R: Register
target26: Absolute operand Z: Zero

## Slide 4: Control Transfer Instructions
 | Mnemonics | Example | Meaning
Conditional Branch | BEQ, BNE, BGEZ, BLEZ, BLTZ, BGTZ | BLTZ R2, -16 | If R2 < 0, PC  PC + 4 -16
Jump | J, JR | J target26 | PC  (PC)31-28¦¦ target26¦¦00
Jump and Link | JAL, JALR | JALR R2 | R31  PC + 8 PC  R2
System call | SYSCALL | SYSCALL | 

## Slide 5: Conditional Branch Instructions
= = != >= 0
Example: BEQ R1,
<= 0 < 0 > 0
R2, -16
Take the branch if contents of R1 = = contents of R2
The target address of the branch is specified using PC relative addressing mode
PC + 4 -16
For examples, we will use a more readable notation BEQ R1, R2, label
 | Mnemonics | Example | Meaning
Conditional Branch | BEQ, BNE, BGEZ, BLEZ, BLTZ, BGTZ | BLTZ R2, -16 | If R2 < 0, PC  PC + 4 -16

## Slide 6: Jump Instructions
 | Mnemonics | Example | Meaning
Jump | J, JR | J target26 J R5 | PC  (PC)31-28¦¦ target26¦¦00 PC  R5
Unconditional control transfer to the instruction at the target address
  Target address specified using absolute addressing mode
  i.e. target address itself included in the jump instruction
  But addresses are also 32b in size: an address won’t fit into a 32b instruction
  MIPS 1 Solution: Include 26bits of target address in the instruction

## Slide 7: Jump and Link Instructions
 | Mnemonics | Example | Meaning
Jump and Link | JAL, JALR | JALR R2 JAL target26 | R31  PC + 8 PC  R2
Unconditional control transfer to the instruction at the target address along with remembering of PC+8 in R31
  Target address specified as in J, JR instructions
  We will see how this instruction is useful in function calls

## Slide 8: C Control Transfer Constructs…
C | MIPS 1 Instructions
goto label | J label
if (X > 0) thenpart; else elsepart | LW R1, X BGTZ R1, thenpart elsepart: : thenpart:
repeat loopbody until ( X != 0) | LW R1, X loophead: loopbody BEQ R1, R0, loophead

## Slide 9: Interesting Notes from ISA Manual.
For load instructions: the loaded value might not be available in the destination register for use by the instruction immediately following the load
  LOAD DELAY SLOT
For control transfer instructions: the transfer of control takes place only following the instruction immediately after the control transfer instruction
  BRANCH DELAY SLOT

## Slide 10: Interesting Notes from ISA Manual.
Warning about Load instructions
LW | R1, | -8(R2)
ADD | R3, | R1, R2

## Slide 11: Interesting Notes from ISA Manual
For load instructions: the loaded value might not be available in the destination register for use by the instruction immediately following the load
  LOAD DELAY SLOT
For control transfer instructions: the transfer of control takes place only following the instruction immediately after the control transfer instruction
  BRANCH DELAY SLOT

## Slide 12: Interesting Notes from ISA Manual.
Warning about Load instructions
LW R1, -8(R2) LW R1, -8(R2)
ADD R3, R1, R2 An instruction that does not use R1
ADD R3, R1, R2
Warning about Control Transfer Instructions
head: loopbody
BEQ R1, R0, head

## Slide 13: Interesting Notes from ISA Manual
For load instructions: the loaded value might not be available in the destination register for use by the instruction immediately following the load
  LOAD DELAY SLOT
For control transfer instructions: the transfer of control takes place only following the instruction immediately after the control transfer instruction
  BRANCH DELAY SLOT

## Slide 14: Interesting Notes from ISA Manual.
Warning about Load instructions
LW R1, -8(R2) LW R1, -8(R2)
ADD R3, R1, R2 An instruction that does not use R1
ADD R3, R1, R2
Warning about Control Transfer Instructions
head: loopbody
BEQ R1, R0, head
head: loopbody
BEQ R1, R0, head next-instruction

## Slide 15: MIPS 1 Instruction Encoding
Example:
add R 1, R 2, R 3
Opcode 6 bits | Src1 5 bits | Src2 5 bits | Dest 5 bits | shift amt 5 bits | Function Code 6b
R Format

## Slide 16: MIPS 1 Instruction Encoding
Opcode 6 bits | Src1 5 bits | Dest 5 bits | Constant 16 bits
I Format
Example:
addi R 1, R 2, 8
lw R 1, 24 (R 2)
bltz R 1, loop

## Slide 17: MIPS 1 Instruction Encoding
Opcode 6 bits | Jump address 26 bits
J Format
Example: jal fact

## Slide 18: Recall: C Program to a.out
% gcc program.c
program.c: File containing program written in the C programming language
a.out: File containing executable equivalent program in machine language

## Slide 19: Steps in gcc
cpp
program.c
cc1
as
ld
hello.s
program.o
a.out
Library files
e.g., math.o, the math library
These are text files – you can read or write them with a text editor
These are object files (binary) – you can write programs to read them